## Slide 1: Deploying Microsoft Azure Stack Hub
Microsoft Azure Stack Hub Architecture
This work is licensed under a Creative Commons Attribution - ShareAlike 4.0 International Public License

## Slide 2: Agenda
Architecture overview
Capacity, scalability, and resiliency
Compute
Networking
Storage

## Slide 3
Delivering Azure Stack Hub as an integrated system
Software
Hardware
Support
Services

## Slide 4: Azure Stack Hub integrated systems
Accelerated time to value
From concept to operations in days, not months
Help developers be productive much faster
Enriched lifecycle management
Greater quality and system reliability
Focus on delivering Azure services, not operations
Continuous innovation
Newest services and fastest updates
Minimize disruption to user availability/experience
...….
….
….

## Slide 5: Azure Stack Hub integrated system
Software
Hardware
Support
Services
Architecture, hardware, and topology
Security and privacy
Deployment, configuration, provisioning
Validation
Monitoring, diagnostics
Business continuity
Patching and updating
Field replacement of parts
BMC Switch
ToR Switch
ToR Switch
Server
Server
Server
Server
Azure Stack Hub
integrated system

## Slide 6
Azure Stack Hub integrated systems

## Slide 7: Azure Stack Hub minimum hardware requirements: Servers
Ratio** of
Cache to Capacity
10%
2 Power Supplies
4+ Capacity Devices
(HDD or SSD)
** Cache capacity should accommodate intended workload.
If Spaces Direct cache devices are used in the solution, the capacity will align with the devices’ resiliency or drive-writes-per-day capabilities. The OEM will provide more details of their solutions’ capabilities for caching
Storage
Compute
2+ Flash Devices
(NVMe, SATA SSD or SAS SSD)
CPU: 20 Cores Minimum (2 socket @ 10 cores each)
256GB Memory Minimum
Boot Device 400GB or larger (optional mirroring)
NIC – 2 port 10 GbE or better

## Slide 8: Azure Stack Hub integrated system (lifecycle)
Architecture, hardware, and topology
Security and privacy
Deployment, configuration, provisioning
Validation
Monitoring, diagnostics
Business continuity
Patching and updating
Field replacement of parts

## Slide 9: Azure Stack Hub hardware requirements: Network switches*
Top-of-rack switches
2 switches per scale unit, configured for resiliency
10 GbE or better for server connectivity
Support for BGP, DCB, PFC, ETS, and Multi-Chassis Link Aggregation
BMC / management network switch
1 GbE switch capable of L3 routing and simultaneous connectivity to the ToRs
*Single scale unit

## Slide 10: Azure Stack Hub architecture overview

## Slide 11: Cloud operating model
use
operate
use
operate
Microsoft engineers
Your customers
Azure customers
Your engineers
Cloud Architect – Design
Cloud Operator – Operate Azure Stack Hub
Azure Stack Hub instance
Azure

## Slide 12: Infrastructure software – What runs where?
Appliance-like architecture and deployment
Servers: Windows Server 2016
Compute / Storage / Network
All infrastructure roles are hosted in VMs
Resiliency, scalability, change in features
VMs get re-deployed during patch and update (replace instead of patch)
These VMs run Windows Server 2016
Azure Stack Hub customer and cloud administrator
Tenant and Admin Portal

## Slide 13: I’m an admin, what’s my focus?
Management of Azure Stack Hub is performed within the portal and cannot be managed like traditional virtualization platform solutions
Traditional Virtualization Management
Cloud-based Management
https://adminportal.local.azurestack.external

## Slide 14: Azure Stack Hub core infrastructure roles
Role Name | components or services description
AzS-ACS01 | Azure Stack Hub storage services.
AzS-ADFS01 | Active Directory Federation Services (ADFS).
AzS-BGPNAT01 | Edge router and provides NAT and VPN capabilities for Azure Stack Hub. (only for ASDK)
AzS-CA01 | Certificate authority services for Azure Stack Hub role services.
AzS-DC01 | Active Directory, DNS, and DHCP services for Microsoft Azure Stack Hub.
AzS-ERCS01 | Emergency Recovery Console VM.
AzS-GWY01 | Edge gateway services such as VPN site-to-site connections for tenant networks.
AzS-NC01 | Network Controller, which manages Azure Stack Hub network services.
AzS-SLB01 | Load balancing multiplexer services in Azure Stack Hub for both tenants and Azure Stack Hub infrastructure services.
AzS-SQL01 | Internal data store for Azure Stack Hub infrastructure roles.
AzS-WAS01 | Azure Stack Hub administrative portal and Azure Resource Manager services.
AzS-WASP01 | Azure Stack Hub user (tenant) portal and Azure Resource Manager services.
AzS-XRP01 | Infrastructure management controller for Microsoft Azure Stack Hub, including the Compute, Network, and Storage resource providers.

## Slide 15: Hardware lifecycle host (HLH)
Definition
A server connected to the BMC Network that is external to the Azure Stack Hub environment
Available to run partner’s lifecycle management software within VMs
Purpose
Hardware monitoring software
Firmware configuration and update software
Emergency management and hardware troubleshooting
Running the Azure Stack Hub Deployment Virtual Machine (DVM) for the duration of initial deployment
Configuration
Network connection to the BMC switch
Windows Server 2016 Standard or Datacenter Edition
Enabled with Hyper-V role
Meets Azure Stack Hub security requirements

## Slide 16: Azure Stack Hub concepts
  Single instance of Azure Resource Manager (ARM)
  1 or more Regions under management of ARM
  Supports different hardware vendors across multiple regions
Cloud
Set of Scale Units that share same “physical location”
Under one physical and logical “administrator”
Networking requirements
  High-bandwidth/low latency
  Flat, layer-3 network
Other attributes are implied by customer choices
Scale unit may have different type of hardware from same vendor
Region
  Associated with a single Region
  1 or more Scale Units within a Region
  Unit of capacity expansion
  4 or more servers within a scale unit
  Fault domains (Azure consistency)
  Alignment of Hardware SKU – which is homogenous within Scale Unit
Scale Unit

## Slide 17
Scale Unit
Border
Device
ToR Switch
ToR Switch
Server
Server
Server
Server
BMC Switch
HLH

## Slide 18
ToR Switch
ToR Switch
Server
Server
Server
Server
BMC Switch
ToR Switch
ToR Switch
Server
Server
Server
Server
Spine Switch
Spine Switch
BMC Switch
……….
Scale Unit 1
Scale Unit n
Border
Device
Region
Cloud
Multiple scale units is still a FUTURE planned capability for Azure Stack Hub. Not available now.

## Slide 19
ToR Switch
ToR Switch
Server
Server
Server
Server
BMC Switch
ToR Switch
ToR Switch
Server
Server
Server
Server
Aggregate Switch
Aggregate Switch
BMC Switch
……….
Space, Power,
& Cooling
Identity Integration
(Tenant & Cloud Admin)
Border
Device
Datacenter monitoring/ticketing/
hardware monitoring
Scale Unit 1
Scale Unit n
Integration in your datacenter

## Slide 20: Azure Stack Hub capacity, scalability, and redundancy

## Slide 21: Azure Stack Hub: Inputs to capacity planning
Servers
Cores
Memory
Storage devices (capacity)
NIC performance
Storage performance
Infrastructure use (VMs + software update)
Application behaviors

## Slide 22: Azure Stack Hub scale unit
Infrastructure Services
Patch and Update Reserve
Tenant Capacity
Server
Server
Server
Server

## Slide 23: Azure Stack Hub scale unit – Adding server nodes…
Infrastructure Services
Patch and Update Reserve
Tenant Capacity
Server
Server
Server
Server
Server
Server
Server
Server
Tenant Capacity
Note – Servers can be added individually up to 16 nodes per scale unit

## Slide 24: Azure Stack Hub Compute

## Slide 25: Compute
Compute
Networking
Storage
Azure Resource Manager
Compute Resource Provider
Azure Guest Agent
Hyper-V Clusters
Storage Accounts
Blobs, Tables, …
vNICs, …
VMs, VM Extensions, Platform Images

## Slide 26: VM sizes on Azure Stack Hub
Azure Stack Hub supports a subset of VM sizes
  Currently we have support for A, D, DS and F
Emulation is imperfect and is focused on uniform in-guest quantities
  RAM, CPU, Disk size quantities are aligned to Azure
  Storage performance is likely to be significantly better than Azure
  CPU performance is better than Azure for low-load environments
  CPU performance is non-deterministic for a given VM size (A VM size may run faster than a Dv2)
Entry level
A
Av2
D
Dv2
DS
General Purpose
DSv2
F
Fv2
Compute Intensive
FS
FSv2
Virtual machine sizes supported in Azure Stack Hub
https://docs.microsoft.com/en-us/azure/azure-stack/user/azure-stack-vm-sizes

## Slide 27: Azure Stack Hub Networking

## Slide 28: Networking
Compute
Networking
Storage
Azure Resource Manager
VMs, VM Extensions, Platform Images
Storage Accounts
Blobs, Tables, …
vNICs, GWs, SLBs, vNets, ACLs…
Network Resource Provider Network Controller Software Load Balancer
Data Plane vSwitch, Gateway

## Slide 29: Physical network switch topology
Two connectivity types in Azure Stack Hub
  DATA (Windows Server 2016 Converged NIC: SDN + Storage)
  BMC (Physical host control + 3rd party hardware monitoring)
Resiliency is built in
  DATA – Single physical NIC with dual ports (minimum 10Gb+)
  Uses switch-embedded-teaming (WS2016) for port/link resiliency
  Assumes dual-switch (ToR) configuration

## Slide 30: Network switch connectivity – within scale unit
BMC Switch
ToR Switch
ToR Switch
Server
Server
Server
Server
BMC – Server Management
Switch Management
Server – Port A
Server – Port B
ToR-to-ToR
MLAG

## Slide 31: Network switch connectivity – between scale units
BMC Switch
ToR Switch
ToR Switch
Server
Server
Server
Server
BMC Switch
ToR Switch
ToR Switch
Server
Server
Server
Server
Aggregate Switch
Aggregate Switch

## Slide 32: Azure Stack Hub Storage

## Slide 33: Storage
Compute
Networking
Storage
Azure Resource Manager
VMs, VM Extensions, Platform Images
SLB, …
Storage Accounts
Blobs, Tables, …
Storage Resource Provider Blob Service, Table Service, …
Scale Out File Server Storage Spaces Direct, ReFS

## Slide 34: Azure-consistent storage
Delivers Azure-consistent Blobs, Tables, and Storage accounts
Comprehensive private cloud service provider manageability
Deployable in either enterprise-private clouds or hosted public clouds from service providers
IaaS storage (Page Blobs), and PaaS storage (Block Blobs, Tables)
Highly-reliable, resilient, and scalable cloud storage based on standard hardware
For Administrator
SMB3 Storage Network Fabric
Storage Spaces, Storage Spaces Direct (S2D), or SAN
Physical Storage
Azure Stack Hub storage cloud admin service
Microsoft Azure Stack Hub w/ SRP
For Tenant
Azure-consistent blob service
Azure-consistent table service
Azure-consistent account service
Scale-Out File Server (SOFS)
. . . . .
Blob back-end
Blob back-end

## Slide 35: Storage stack
Storage Spaces
Single scalable pool with all disk devices (except boot)
Multiple virtual disks per pool (Mirrored)
Software Storage Bus
Storage Bus Cache
Leverages SMB3 and SMB Direct
Servers with local disks
SATA, SAS, and NVMe based on OEM SKU
Storage Spaces Storage Pool
Storage Spaces Virtual Disks
CSVFS Cluster File System
Software Storage Bus
Virtual Machines
ReFS On-Disk File System

## Slide 36: Built-in cache
SATA
SSD
SATA
SSD
SATA
HDD
SATA
HDD
SATA
HDD
SATA
HDD
SATA
HDD
SATA
HDD
Caching devices
Capacity devices
Cache is an integral part of Software Storage Bus
Scoped to local machine
Agnostic to storage pool and virtual disks
Automatic configuration when enabling Spaces Direct
Cache behavior is dependent on type of operation

## Slide 37: Azure Stack Hub volumes
Mirror spaces have resiliency granted from multiple data copies
Like Azure, data has three copies in Azure Stack Hub
Azure Stack Hub leverages a 3-way mirror
Normal mirror sets can survive the loss of a single physical disk
Azure Stack Hub 3-way mirror can survive the loss of two physical disks
Category | Detail
Volume type | Mirror
Optimized for | Performance
Use case | All data is hot
Efficiency | Least (33%)
File System | ReFS

## Slide 38: Azure Stack Hub storage
Virtual Disks
Infrastructure
Temp Storage (one per server)
Tenant (logically – one per server; managed by ACS)
Add a Server
Add one Temp Storage virtual disk
Add one Tenant virtual disk
Mirrored (3-way for Infrastructure and Tenant) Physical Devices
2 or more Storage Spaces Direct cache devices
4 or more Storage Spaces Direct capacity devices

## Slide 39: Azure Stack Hub storage redundancy
Server 1
Server 2
Server 3
COPY #0001
COPY #0002
256 MB #0003
256 MB #0004
COPY #0004
256 MB #0005
256 MB #0006
COPY #0006
256 MB #0007
256 MB #0001
256 MB #0002
COPY #0003
COPY #0005
COPY #0007
256 MB #0008
COPY #0008
256 MB #0009
COPY #0009
COPY #0010
256 MB #0010
COPY #0011
256 MB #0011
COPY #0012
256 MB #0012
COPY #0013
256 MB #0013
COPY #0014
256 MB #0014
COPY #0015
256 MB #0015
COPY #0016
256 MB #0016
COPY #0017
256 MB #0017
COPY #0018
256 MB #0018
COPY #0019
256 MB #0019
COPY #0020
256 MB #0020
COPY #0021
256 MB #0021
COPY #0022
256 MB #0022
COPY #0023
256 MB #0023
COPY #0024
256 MB #0024
In Storage Spaces Direct for Azure Stack Hub, the default is to keep three copies of the data split between three server nodes
Azure Stack Hub VMs are clustered and split across three nodes
Three copies of all data written to disk
This means you can lose a whole server due to failure or during patch and update and still have 2-copy redundancy

## Slide 40: Survival examples

## Slide 41: Azure Stack Hub scale unit resiliency
Switch resiliency
A single TOR or Aggregate switch can fail
PDU resiliency
A single power supply or PDU can fail with no issues
Server resiliency
A single Server node can fail, as long as disk failures are limited to one other Server node
A third Server node down or failed disks in a third Server node will take the affected virtual disks offline
Disk resiliency
A single disk can fail anywhere in the scale unit
Multiple disks can fail, as long as they are limited to two server nodes

## Slide 42: Questions?

## Slide 44
Logical network diagram