## Slide 1: Managing Microsoft Azure Stack Hub
Microsoft Azure Stack Hub Control Plane Monitoring
This work is licensed under a Creative Commons Attribution - ShareAlike 4.0 International Public License

## Slide 2: Agenda
Azure Stack Hub Admin philosophy
  Management and monitoring basics
Monitoring Azure Stack Hub
  Alert remediation
  Capacity
  Azure Monitor on Azure Stack Hub
Integrating with Existing Tools
  Infrastructure integration
  SCOM, Nagios, other tools

## Slide 3: Basics of Azure Stack Hub Management and Monitoring: Azure Stack Hub Components

## Slide 4: Azure Stack Hub monitoring
Azure Stack Hub software components internally monitored via
Health Services
Service Fabric Health
Metrics and Logs centrally collected
Hardware monitoring
  OEMs responsible for agentless HW device monitoring/validation through external systems (monitor nodes/switches)
      This is done by each OEM adding a VM to Azure Stack Hub called the Hardware Lifecycle Host
  S2D storage monitored by Azure Stack Hub components
REST API for 3rd party integration of alerts, metrics, and logs
  SCOM Azure Stack Hub Fabric MP
  Nagios integration
OEM HW Nodes
Azure Stack Hub Software Components Health & Alerts visible in Admin Portal
Alerts generated from:
  Internal Health Services
    WSHS
    Service Fabric
  Azure Stack Hub components
Rest API available for 3rd Party System Integration
OEM Network Switches
Azure Stack Hub Instance
External Monitoring Systems
Monitoring via SNMP
Restful
Integration
Hardware Lifecycle Host VM (HLH)
Agentless device Monitoring

## Slide 5: Infrastructure Resource Providers overview
Fabric, health, and updates: FRP – HRP – URP
Enable communication with the underlying infrastructure Roles and Hardware Layer
Microservices running in the Infrastructure Service Ring
Can only be called with the Admin Subscription
Each RP provides a northbound API REST API
  Consumed by UX – Portal, PowerShell, Visual Studio, and other tools
Each RP uses a southbound API to communicate with Controllers
HRP and URP provide registration interface for ARM deployable RPs
Templates/PowerShell/CLI, SDK, etc.
Azure Resource Manager (ARM)
RP LAYER
PARTITION REQUEST BROKER
FRP
URP
ARM LAYER
Azure Portal (UX)
HRP

## Slide 6
Physical Node Manager
FRP
Hardware
Infrastructure Role
LDAP/Radius
Network Switch
Radius
DS
Radius
Health
Out of Band Health Monitoring – Agent less using
external monitoring entity such as System Center Operations Manager or Nagios
BMC (IPMI) *dedicated NIC
ARM
Portal/UX
NRP
…
Network Controller
…
Power On
Power Off
Recycle Power
Can use external Radius
LDAP or Radius
Infra
Deployment
Change Boot Order – Clear / Get SEL logs
Azure Stack Hub
As an admin, you use Portal/ARM/CLI to ask the Fabric Resource Provider to perform an action…
Here are some example actions…
And the action will be performed by the appropriate Azure Stack Hub service…
Hardware management diagram

## Slide 7: Monitoring Azure Stack Hub

## Slide 8: Monitoring problem space
Complexity of understanding health
Clouds depend on many different technologies
Health of the cloud is not the sum of its parts
How do alerts relate to health?
Tax of alert deciphering
  Which alerts do I need to take action on?
  Which alerts should I address first?
  What are the steps to resolve?

## Slide 9: Azure Stack Hub monitoring philosophy
Health is shown through ALERTS
The alerts are managed by the Health Resource Provider (HRP)
You can consume these alerts to suit your own tools and processes
Azure Stack Hub manages and monitors all of the software in the box
OEM will provide management capabilities for the hardware (including in-box network switches)
The Hardware Lifecycle Host VM, which is OEM-specific, hosts these hardware management roles (and can be the target location to store logs pulled from an Azure Stack Hub scale unit during troubleshooting)
  Th

## Slide 10: Monitoring and operation: Core principles
Azure Stack Hub is designed to be treated like an appliance
Majority of a cloud admin’s interaction with Azure Stack Hub should be driven by Alerts (if it’s not broken, don’t touch it)
Azure Stack Hub component health should be directly tied to Alerts
Alerts should be
Easy to understand impact and next steps
Resolved using common Azure Stack Hub Admin action patterns
Specific to Azure Stack Hub

## Slide 11: Azure Stack Hub infra, HW monitoring & integration overview
Network switches monitored via SNMP
External Monitoring Solution
HRP Rest API
Windows Server Health Service Alerts for:
Physical Disks
Network Adapters
Node
Agentless monitoring of hyper-converged hardware using BMC. Solution dependent on hardware vendor.
Azure Stack Hub alerts can be consumed by external monitoring solutions
Datacenter network

## Slide 12: Alert and remediation examples
Alert name | Severity | Component | Alert remediation
An infrastructure role is unresponsive | Critical | Compute controller | Navigate to the compute controller infrastructure role and restart the role If the issue persists, contact support
Low memory capacity in Azure Stack Hub region | Warning | Capacity management | Add a node to the scale unit using the capacity management admin blade
A physical disk has failed | Warning | Capacity management | The physical disk located <Location Info> has failed. The process of repairing the storage virtual disk has been initiated. It is important to replace the physical disk to ensure full capacity and resiliency. Click on this to learn more about performing the disk replacement procedure.

## Slide 13: Azure Monitor on Azure Stack Hub

## Slide 14: Azure Monitor for Azure Stack Hub
Azure Monitor is the platform service that provides a single source for monitoring Azure resources. With Azure Monitor, you can visualize, query, route, archive, and otherwise take action on the metrics and logs coming from resources in Azure Stack Hub with experiences consistent with Azure. You can work with this data by using the Azure Stack Hub admin portal, Monitor PowerShell Cmdlets, Cross-Platform CLI, or Azure Monitor REST APIs
Azure Monitor on Azure Stack Hub provides metrics for the compute and storage services, with additional services to be added in the future

## Slide 15: Application - Diagnostics logs, Application logs, and Metrics
Applications can run in the OS of a VM running with the Microsoft.Compute resource provider. These applications and VMs emit their own set of logs and metrics. Azure Monitor relies on the Azure diagnostics extension (Windows or Linux) to collect most application level metrics and logs
The types of measures include:
  Performance counters
  Application logs
  Windows event logs
  .NET event source
  IIS logs
  Manifest-based ETW
  Crash dumps
  Customer error logs

## Slide 16: Uses for monitoring data
Store and Archive
Some monitoring data is already stored and available in Azure Monitor for a set amount of time
Metrics are stored for 90 days
Activity log entries are stored for 90 days
Diagnostics logs are not stored
Archive the data to a storage account for longer retention (work in progress as of November 2018)
Query
You can use the Azure Monitor REST API, cross-platform Command-Line Interface (CLI) commands, PowerShell cmdlets, or the .NET SDK to access the data in the system or Azure storage

## Slide 17: Uses for monitoring data
Visualization
Visualizing your monitoring data in graphics and charts helps you find trends quicker than looking through the data itself
A few visualization methods include:
Use the Azure Stack Hub user and admin portal
Route data to Microsoft Power BI
Route the data to a third-party visualization tool using either live streaming or by having the tool read from an archive in Azure storage

## Slide 18: Methods of accessing Azure monitor on Azure Stack Hub
In general, you can manipulate data tracking, routing, and retrieval using one of the following methods. Not all methods are available for all actions or data types.
Azure Stack Hub Portal
PowerShell
Cross-platform Command Line Interface(CLI)
REST API
.NET SDK

## Slide 19: How the Health Resource Provider Works

## Slide 20: What is HRP?
Health Resource Provider
Resource provider that provides and allows actions on Azure Stack Hub Alerts
Resource provider that collects and displays metric data
Runs as a Service Fabric service in the ‘XRP’ VM
The HRP provides a list of Resource Providers and Infrastructure Roles to the portal UI that allows an administrator to assess the health of Azure Stack Hub elements.

## Slide 21: Data flow overview
1
2
3
4
Raw data collected from hosts and VMs.
  Faults
  Metric data
  Heartbeats
  Telemetry events
  Audit logs
Monitoring system accesses the RAW data to process:
  Faults => Alerts
  Metrics aggregation
  Delete old data
Telemetry subsystem extracts telemetry events and sends them to Microsoft through normal telemetry interface (UTC)
  Data is later analyzed at Microsoft to understand stamp behavior (telemetry sending can be disabled)
  We upload all Alerts
Response to external component calls:
  Alert list and details
  Region Health
  List of registered RPs and Resources
Admin Portal

## Slide 22: Registration with monitoring
All foundational RPs are registered with HRP during deployment (or redeployment during patch and update)
  Value-add RPs, like SQL/MySQL do not currently register with HRP, but that is the intention for future enhancement
Each registration provides:
  RP Display Name
  Storage Account dedicated to monitoring
  Alert templates
Infra resources are also registered and linked to RP
The registration data is used to determine which RPs/resources are healthy and which require attention
Alert templates determine which alerts will be shown to the user
  Each RP therefore defines its own alerts and declares them to the HRP

## Slide 23: Alert Remediation for Azure Stack Hub Infrastructure

## Slide 24: Infrastructure operations (Actions)
Principles:
Administrative actions driven by alerts
Resource action hierarchy – how actions are applied when recovering functionality
(Some scenarios may require Privileged Endpoint access)
Resources | Available Actions
Infrastructure Role Instance | Start, Shutdown, Restart
Scale Unit Node | Repair, Drain/Resume, Shutdown, Power Off, Power On

## Slide 25: Infrastructure role instances
Example scenario: An Infrastructure Role Instance is unresponsive and its functionality needs to be restored.
Available Actions
Start
Shutdown
Restart*
*Restart is implemented as a logic that orchestrates
  Shutdown (Guest OS using IC), Turn Off VM, Start VM
Fabric RP
Compute Controller
Hyper-V

## Slide 26: Scale unit node – Part 1
Example scenario: A Scale Unit Node is not responsive and its functionality needs to be restored.
Available Actions
Drain/Resume
Power On/Off
Fabric RP
Compute Controller
Enterprise Cloud Engn
Fabric RP
Compute Controller
Failover Clustering
IPMI
BMC

## Slide 27: Scale unit node – Part 2
Available Actions
Repair
Fabric RP
Enterprise Cloud Engine
Failover Clustering
Storage Controller
Azure-Consistent Storage
Compute Controller
1
2
Compute
Storage
Make Physical Server available as compute resource
Add storage to the Storage Pool
  Supported Scenarios
    Data Drives Healthy
    Bad Data Drives
  Not supported
    Dirty Drives
The ECE splits the repair request into two parts – disk and compute
Provision from bare metal and add node to scale unit’s cluster
If the disks have data, keep it. If not, wipe and add to storage spaces…

## Slide 28: FRU – Field Replacement Unit
Example scenario: Scale Unit Node does not respond because of a damaged motherboard.
Enable Maintenance Mode (drain)
Turn Off
Turn On
Check alert resolved
Replace Part
Repair Node
Disable Maintenance Mode (resume)
Ability to use KVM Viewer
Alert
OEM

## Slide 29: What happens if I can’t use the actions?
Example scenarios: Portal, ARM, Fabric Resource Provider, Directory Service or Storage are offline?
Service Provider
Machine
Privileged Endpoint
Infrastructure Role Instances
Microsoft Support
Receives Diagnostic Package
Provides 2nd Phase for Two Way Factor Authentication
Shadows Azure Stack Hub troubleshooting ( Screen Sharing)
Guides Service Provider
Service Provider
Create Diagnostic Package
Start Unlock Process
Receives 2nd Phase Key from Support
Drives all input activity
PS only
JEA
JEA
GMSA Domain Admin Account
This account is like the server recovery console account in Windows

## Slide 30: Capacity Management

## Slide 31: Basic – View/manage capacity using the portal
Goals
Retrieve Alerts for resources running low on capacity
Visualize resource usage (Memory, Storage, IP pools)
Add resources (for example, IP address space)
More advanced
Use alerts and metrics to feed an external tool for capacity management and planning

## Slide 32: IP pools
Example scenario: I am running out of IP space for my external VIPs.
Available Actions
Get-AZsIpPool – List IP pools
Add-AZsIpPool - Adds IP pool
  No size restrictions for expansion
  Only deployment has an initial size requirement (based on VIPs)
Example:
Add-AzsIpPool -Name "PoolName" -StartIPAddress "192.168.55.1" -EndIPAddress "192.168.55.254" -AddressPrefix "192.168.55.0/24"
FRP
NC

## Slide 33: Decision conversation – Connecting outside Azure Stack Hub
For your initial deployment, can you use alerts, health, and capacity information as exposed in the Azure Stack Hub portal, or do you need to connect to external monitoring/capacity/ticketing systems?

## Slide 34: How to Talk to Azure Stack Hub

## Slide 35: API integration principles
ARM
FRP/HRP/URP
Authenticate with AAD
Retrieve a Token for Admin Subscription
Call API Namespace with Action
  Health Resource Provider (HRP) https://Host:30005/subscriptions/9d334843-0c6e-4bfc-b82c-cf229da3a87b/resourcegroups/System/providers/Microsoft.InfrastructureInsights.Admin
AAD
Tool
Health Controller
1
2
3
To query Azure Stack Hub state and health, you must connect with sufficient authorization and use APIs to talk to the Fabric, Health, or Update Resource Providers…
Azure Stack Hub administrator REST API detail is here - https://docs.microsoft.com/en-us/rest/api/azure-stack/

## Slide 36: Fabric RP – API resources
Namespace resources
Location (Region)
Infrastructure Roles
Logical Networks
Storage Subsystem
File Shares
Role Instances
Scale Units
  Physical Server
Actions:
Get, Put, Post

## Slide 37: Health RP – API resources
Namespace resources
Location (Region)
Alert
Service Health Registrations
Resource Health Registration
$URI="${ArmEndpoint}/subscriptions/${subscription}/resourceGroups/system/providers/Microsoft.InfrastructureInsights.Admin/regionHealths/$region/Alerts?api-version=2016-05-01"
$Alert=Invoke-RestMethod -Method GET -Uri $uri -ContentType 'application/json' -Headers $Headers
$Alerts=$Alert.value
$Alertsprop=$alerts.properties
$Alertsprop |select alertid,state,title,resourcename,createdtimestamp,remediation
Example – query an Azure Stack Hub region of a subscription for current alert properties
Actions:
Get
Put
Delete

## Slide 38: Update RP – API resources
Namespace resources
Location (Region)
Region Update Status
Updates
  Update Runs
Actions:
Get
Put

## Slide 39: Monitoring and Integrating with the ‘Bigger Picture’ Azure Stack Hub-Related Systems in Your Datacenter

## Slide 40: ITSM integration
Enable IT Service Management by adopting existing pipes
Monitor with existing datacenter monitoring tooling
Use existing connections from monitoring to ticketing and others
Azure Stack Hub Software*
*including Storage
Physical Server
Network Devices
Monitoring Solution
Ticketing, CMDB…
Integrated System
Rest API
BMC
SNMP

## Slide 41: Monitoring integration solutions
  Azure Stack Hub Software – API
  Nagios Plugin (for Open Source & Enterprise Edition) (Available today http://aka.ms/masnagios)
  API examples and documentation for custom integration (GitHub)
  System Center Operations Manager – Management Pack
  Physical Server – BMC
  System Center Operations Manager – Hardware Vendor Management Pack
  Hardware Vendor Nagios Plugins
  Other OEM supported monitoring solutions
  Network Devices – SNMP
  System Center Operations Manager – Network Device Discovery
  Nagios Switch Plugin
  Other OEM supported monitoring solutions
  Tenant Subscription Health Monitoring
  System Center Operations Manager – Azure Management Pack
  Operations Management Suite (OMS)

## Slide 43: Hardware monitoring and ITSM Integration
Hardware monitoring
Azure Stack Hub will natively surface alerts for Physical Disks, JBODs, and Node failures
All other hardware monitoring will be provided by OEMs using external monitoring tools (SCOM, etc.)
  Network Switch monitoring via SNMP
  Physical Server monitoring via existing OEM provided agentless monitoring solutions
  Implemented on the Hardware Lifecycle Host VM
Enable ITSM by adopting existing pipes
  Monitor with existing datacenter monitoring tooling
  Use existing connections from monitoring to ticketing systems
      Microsoft will provide:
          Azure Stack Hub Management Pack for SCOM
          Azure Stack Hub Open Source a module for Nagios and support for Nagios Enterprise
          Azure Management Pack for Azure Stack Hub Tenant Subscription monitoring using SCOM
          API documentation to be used for custom integration

## Slide 44: Additional info
Monitoring and updating examples and details:
https://github.com/Azure/AzureStack-Tools/tree/master/Infrastructure
Master list of Azure Stack Hub commands:
https://github.com/Azure/AzureStack-Tools/tree/master/Infrastructure

## Slide 45: Health Resource Provider Troubleshooting

## Slide 46: Common issues
HRP service cannot access Health storage accounts
Data not flowing to storage accounts from nodes/VMs
HRP services are offline

## Slide 47: HRP service cannot access storage accounts
Impact
The monitoring system will not be able to create new alerts, collect telemetry, or update metrics data for specific RP/resource
Data will not be pruned
This issue can occur when storage is down globally or when storage keys were rotated and monitoring system was not updated
Alerts
  Administrator will be presented with alerts around storage not available
  There may be some already-closed alerts right at setup time. This is a result of some extra-early health assessments while Azure Stack Hub goes through first time setup
Potential resolution
  If storage is available for everyone else, try to rotate storage keys
  If storage is offline, look for other alerts related to storage

## Slide 48: Data not flowing to storage accounts
Impact
  Data collected on a host or VM does not leave the OS instance
  Once enough time passes the local data will start being overwritten, causing potential loss in monitoring data
  Alerts
  The monitoring service will notice missing data and display missing host/VM alert
  Possible resolutions
  This could be caused by an issue in storage or networking. Look for alerts in those areas to understand what is going on

## Slide 49: HRP services are offline
Impact
  The Administrator UX does not display list of RPs, Resources, or Infra Roles
  The affected region is missing in the region list in admin UX
  List of regions and region health cannot be retrieved
  The SCOM and Nagios integration is broken
  Alerts
  None, customer must rely on external system
  Potential resolution
  Restart Health Service Fabric applications – this will require a call to support to get the required access…

## Slide 50: HRP services are offline - Troubleshooting
Support will guide the operations team to get PowerShell access to the Privileged Endpoint
Use PowerShell cmdlets to restart Health SF applications
Use Fabric RP API to restart Health role
If HealthService in either RP or AzurestackHealth is offline the application will appear offline
List of fabric applications…

## Slide 51: Getting details from diagnostic data
All components of Monitoring follow the same diagnostics pattern as rest of Azure Stack Hub. Use Get-ASEvent and Get-ASChildEvent cmdlets to filter data.
Event provider names:
  Microsoft-AzureStack-Health
  Microsoft-AzureStack-Health-WebApi
  Microsoft-AzureStack-Common-Infrastructure-Http
You can use common practices developed across the components to get further details from the log data.

## Slide 52: Questions?

## Slide 54: Azure Stack Hub architecture overview
Templates/PowerShell/CLI, SDK, etc.
Azure Resource Manager (ARM)
RP LAYER
PARTITION REQUEST BROKER
SRP
NRP
FRP
CRP
URP
Infrastructure Deployment
Bootstrap
Patch & Update
Scale Out
FRU
RESET
START
STOP
COMPUTE CONTROLLER
STORAGE CONTROLLER
NETWORK CONTROLLER
INFRA ROLE CONTROLLER
HEALTH CONTROLLER
ARM LAYER
INFRASTRUCTURE CONTROL LAYER
Azure Portal (UX)
Builds
COMPUTE
NETWORK (SWITCHES)
STORAGE
HARDWARE LAYER
Workflows
HRP
…
PHYSICAL
NODE
MANAGEMENT
INFRASTRUCTURE ROLES
The Azure Stack Hub infrastructure roles are like the task manager in Windows. You know there are things going on, but you don’t need to understand them all, or manage them.

## Slide 55: Azure Stack Hub architecture overview
Templates/PowerShell/CLI, SDK, etc.
Azure Resource Manager (ARM)
RP LAYER
PARTITION REQUEST BROKER
SRP
NRP
FRP
CRP
URP
Infrastructure Deployment
Bootstrap
Patch & Update
Scale Out
FRU
RESET
START
STOP
COMPUTE CONTROLLER
STORAGE CONTROLLER
NETWORK CONTROLLER
INFRA ROLE CONTROLLER
HEALTH CONTROLLER
ARM LAYER
INFRASTRUCTURE CONTROL LAYER
Azure Portal (UX)
Builds
Workflows
HRP
…
PHYSICAL
NODE
MANAGEMENT
ADFS
DIRECTORY MGMT
ACS
PHYSICAL NODE MGMT
EDGE GATEWAY
LB MUX
INTERNAL DATA STORE
UPDATE MGMT
CERTIFICATE MGMT
INFRASTRUCTURE ROLES
STORAGE CONTROLLER
COMPUTE CONTROLLER
NETWORK CONTROLLER
INFRA ROLE CONTROLLER
HEALTH CONTROLLER
INFRA DEPLOYMENT
PARTITION
REQ BROKER
INFRA MGMT
CONTROLLER
ARM
COMPUTE
NETWORK (SWITCHES)
STORAGE
HARDWARE LAYER
You don’t need to know how to manage or troubleshoot these…

## Slide 56: Azure Stack Hub monitoring architecture overview
Health RP
Azure Resource Manager (ARM)
Exposes
Health
Alerts
Metrics, log, & security audit storage locations
Health Service
Alert Service
Registration for
Resource Providers
Infra Services
Alert service generates Alerts based on ETW Events in RP specific storage accounts
RP Layer
Fabric Control Layer
ARM / Portal Layer
OS / Physical Infra layer
Azure Monitoring Agent (MA) collects the following for all Azure Stack Hub SW components:
ETW Events
Metrics
Logs
All data written to RP-specific Storage account with specific containers as shown below
Service Fabric Ring
Registration Data
Alert Data
Security Container
Resource Provider’s Storage Account
Fault Container
Metric Container
Diagnostic Container
Key concept – monitoring information is placed into a storage account within Azure Stack Hub

## Slide 57: FRP call flow example – Allocate a VM
Templates/PowerShell/CLI, SDK, etc.
Azure Resource Manager (ARM)
RP LAYER
PARTITION REQUEST BROKER
SRP
NRP
FRP
CRP
URP
COMPUTE CONTROLLER
STORAGE CONTROLLER
NETWORK CONTROLLER
INFRA ROLE CONTROLLER
HEALTH CONTROLLER
ARM LAYER
INFRASTRUCTURE CONTROL LAYER
Azure Portal (UX)
COMPUTE
NETWORK (SWITCHES)
STORAGE
HARDWARE LAYER
HRP
…
PHYSICAL
NODE
MANAGEMENT
OS LAYER
Windows Server Node/Hyper-V

## Slide 58: FRP – Physical node management
Interacts with physical servers
Using “PcsvDevice” IPMI implementation
Authenticates using BMC Account or LDAP (Recommended for Larger Scale)
FRP Securely Stores BMC Credentials
Physical Node Management (PNM)
Hardware – Base Board Management Controller
Power On
Power Off
Power Cycle
Clear Log
Get Log
Set Boot Device
Discovery
FRP

## Slide 59: FRP – Infrastructure Role Controller
Interacts with Infrastructure Roles (Lifecycle Management)
Windows Auth to interact with Hosting Platform (SF, FC, WS, IIS)
  Protocol based on Hosting Platform as well
Infrastructure Role Controller (IRC)
Infrastructure Roles / Role Instances
Role Instance Actions (restart, start, stop)
Patch and Upgrade
FRP

## Slide 60: Computer Controller
Interacts with Scale Unit and Hyper-V to manage Virtual Machines
Using PowerShell implementation
Authenticates and authorizes using PowerShell Just-Enough-Admin (JEA)
Computer Controller (CC)
Scale Units / Hyper-V
VM Placement
VM Actions
VM Configuration
Manage Scale Unit Lifecycle
FRP
CRP

## Slide 61: Storage Controller
Interacts with Storage Subsystem
Using PowerShell implementation
Authenticates and authorizes using PowerShell Just-Enough-Admin (JEA)
Storage Controller (SC)
SOFS / S2D
Pools
Volumes
Shares
FRP
SRP