## Slide 1: Disaster Recovery and High Availability
Azure Stack Hub Business Continuity and Disaster Recovery
This work is licensed under a Creative Commons Attribution - ShareAlike 4.0 International Public License

## Slide 2: Agenda
Overview
Infrastructure Backup and Cloud Recovery
HA and DR Patterns
User Backup and Restore
Protecting Workloads
DevOps and BC/DR

## Slide 3: Overview

## Slide 4
BC/DR consistency between Azure and Azure Stack Hub is a journey that continues to progress as capabilities are added over time.

## Slide 5: Topics for today
Azure Stack Hub
I can protect applications deployed on IaaS
I can create a protection strategy for PaaS based
I can recover Azure Stack Hub infrastructure
Operator
Managed Services Provider
Cloud user

## Slide 6: Level set on terminology
Business Continuity and Disaster Recovery (BC/DR)
    BC/DR are closely related practices that describe an organization's preparation for unforeseen risks to continued operations
    BC/DR refers to a strategy that a company implements
    The implementation of a BC/DR strategy will determine the protection schemes technologies that will help a company achieve their recovery objectives
For the purposes of this discussion, we need to start by level setting on some concepts:
    Site level availability
    Physical and logical layering within a cloud
    Fault tolerance within a scale-unit

## Slide 7: Deployment site
Utility Feed
Auto transfer switch (ATS)
Backup generator
N: Tier I
N+1: Tier II
UPS
N: Tier I
N+1: Tier II
Mechanical
Active:
Tier 1 and II
https://uptimeinstitute.com/resources/asset/tier-standard-topology
Uninterruptible power supply
Site

## Slide 8: Deployment site
Utility Feed A
Auto transfer switch (ATS)
Backup generator
N: Tier III
N+1: Tier IV
UPS
N: Tier III
N+1: Tier IV
Mechanical
Active:
Tier III and IV
Backup generator
N: Tier III
N+1: Tier IV
Auto transfer switch (ATS)
Utility Feed B
UPS
N: Tier III
N+1: Tier IV
Mechanical
Passive:
Tier III
Active:
Tier IV
https://uptimeinstitute.com/resources/asset/tier-standard-topology
Site
Azure
Stack
Azure
Stack
Azure
Stack

## Slide 9: Site level failure
Utility Feed A
Auto transfer switch (ATS)
Backup generator
N: Tier III
N+1: Tier IV
UPS
N: Tier III
N+1: Tier IV
Mechanical
Active:
Tier III and IV
Backup generator
N: Tier III
N+1: Tier IV
Auto transfer switch (ATS)
Utility Feed B
UPS
N: Tier III
N+1: Tier IV
Mechanical
Passive:
Tier III
Active:
Tier IV
Impact radius of a disaster
Site
Azure
Stack

## Slide 10
PDU
Rack
PDU
UPS
UPS
Scale-unit
Leaf Switch (ToR)
Leaf Switch (ToR)
Node1
Node(n)
Node16
Node2
BMC Switch
Hardware Lifecycle Host
Layer 3: BGP or Static route
Border Devices
Power distribution unit

## Slide 11: Scale-units do not stretch across datacenters or sites
Scale-unit
Site level high availability: No
Site-aware workloads placement: No
Workload affinity to a site: No
Scale-unit node
Scale-unit node
Scale-unit node
Scale-unit node
Scale-unit node
Scale-unit node
Scale-unit node
Scale-unit node
10km
Site
Site

## Slide 12: Fault tolerance within a scale-unit
Rack
Scale-unit
Administrator and user connectivity:
Top of rack switches (2):
4 uplinks to pair of border devices
Failure impact: None; one switch can handle all traffic
Scale-unit nodes
4-16 nodes configured in highly available topology
Hardware management:
BMC switch (1):
Impact: HW monitoring, some admin operations
Hardware Lifecycle host (1):
Impact: HW monitoring, some admin operations
Leaf Switch (ToR)
Leaf Switch (ToR)
Node1
Node(n)
Node16
Node2
BMC Switch
Hardware Lifecycle Host
Layer 3: BGP or Static route
Border Devices

## Slide 13: Fault tolerance within a scale-unit node
Node
NIC
NIC
Power Supply
Power Supply
Boot
Drive
(if installed)
PDU
PDU
BMC
Leaf Switch (ToR)
Leaf Switch (ToR)
Boot Drive

## Slide 14: Azure Stack Hub Integrated System Single region/single scale-unit deployment
One set of mgmt and portal endpoints
1 region
1 scale units per region
4-16 scale-unit nodes
Azure Stack Hub services and user apps/data deployed across
A
B
C
D
Site
Datacenter/Co-location/Room/Row
Rack
Cloud
https://portal.mycloud.contoso.com https://adminportal.mycloud.contoso.com
Azure Resource Manager
A
Region (1)
Scale-unit (1)
Scale-unit nodes (4-16)
B
C
D
Applications and data
Azure Stack Hub Services
E
E

## Slide 15: But as an admin, I still protect it like a virtual stack?
No!
Protecting, healing, and recovering Azure Stack Hub is fundamentally different from what you do today in Hyper-V environment
  Co-engineered integrated solution
    OEMs are the only authorized entity that can deliver deployment services
    Recovering Azure Stack Hub will involve professional services
    If hardware is unrecoverable, need to account for ordering a new solution
  Appliance experience
    Managed through admin portal – no Hyper-V Manager, no Failover Cluster Manager
    There are no third-party agents installed on an Azure Stack Hub scale-unit’s fabric
    All software on all nodes (including HLH) whitelisted by Microsoft
  Locked down by default
    Network ACLs limit traffic flow to pre-defined paths
    Administrator access limited to break glass procedure through privileged endpoint

## Slide 16: Do I still have a “catch-all” insurance policy?
No!
Protection of resources and resource data in Azure and Azure Stack Hub is a user responsibility
  no way to backup or replicate data from the underlying hypervisor nodes
  no bulk recovery of VMs directly into hypervisor nodes
  The “catch-all” mechanism in Azure (GRS/RA-GRS) is not available in Azure Stack Hub yet
Modern apps (e.g. container, microservices) require a different approach to backup-recovery and disaster-recovery

## Slide 17: Infrastructure Backup

## Slide 18: Azure Stack Hub Infrastructure
Azure Stack Hub
I can protect applications deployed on IaaS
I can create a protection strategy for PaaS based
Infra backup
Cloud Recovery
Operator
Recover Azure Stack Hub data with the Infrastructure Backup Service - Azure Stack Hub | Microsoft Docs

## Slide 19: Infrastructure Backup Controller
Backup Details
  Full backups supported; incremental backups supported in 2102 and above.
  Full backups only (~10 GB)
  Encrypted using .NET libraries
  Can be automatically scheduled (following update 1807)
  Backup does not include network switch or hardware management server configuration.
    Deployment documentation will include steps for backup of this data on the same external infrastructure backup share

## Slide 20: Infrastructure backup requirements
Backup share
  Customer provides SMB3 file share with at least 1TB of available capacity per cloud
    \\fileserver\fileshare\
  Customer must provide a subfolder layout for separate deployments
    \\fileserver\fileshare\<subfolder>\
      Customer can use the same file share for multiple deployments (unique subfolder for each deployment)
  File share must not be hosted on Azure Stack Hub or the HLH
  Azure files currently not supported as a backup location
Backup share credential
  Customer provides an account with read/write access to the share
Encryption key
  Symmetric key required to encrypt backup payload before it is placed on external share

## Slide 21: Configuring backups – The process
Provide backup storage UNC path in admin portal or PowerShell
Provide username and password to backup share
Provide a backup frequency in hours between 4 and 12
Set retention period in days, between 2 and 14. (Backups older than maximum retention period are deleted)
Provide pre-shared key to encrypt backup files

## Slide 22: Infrastructure backup requirements
Share path examples:
Share path | Content | Managed by
\\fs01.contoso.com\AzSBackups\mast.contoso.com\nyc\HLH | Hardware lifecycle host config and data | Customer
\\fs01.contoso.com\AzSBackups\mast.contoso.com\nyc\Switches | ToR/BMC switch config | Customer
\\fs01.contoso.com\AzSBackups\mast.contoso.com\nyc\DeploymentData | Generated files for deployment | Customer
\\fs01.contoso.com\AzSBackups\mast.contoso.com\nyc\Registration | Activation data | Customer
Share path | Content | Managed by
\\fs01.contoso.com\AzSBackups | Can contain backups from one or more Azure Stack Hub clouds | Customer
\\fs01.contoso.com\AzSBackups\mast.contoso.com | Backups from deployments that use mast.contoso.com external FQDN | Customer
\\fs01.contoso.com\AzSBackups\mast.contoso.com\nyc | Backup data for region called NYC | Customer
\\fs01.contoso.com\AzSBackups\mast.contoso.com\nyc\MASBackup | Azure Stack Hub infra backup data | Azure Stack Hub
NYC region subfolder examples:

## Slide 23: Infrastructure backup controller
Azure Stack Hub separates infrastructure data from tenant data
  Tenants of Azure Stack Hub are responsible for protecting their workloads and backing up data
  Infrastructure data from multiple internal services is backed up by Azure Stack Hub using the Infrastructure Backup Controller service
Backup Configuration
  Backup occurs periodically with no admin intervention and no downtime to the portal experience or APIs
  Backup data is stored to an external/off-stamp SMB file share
  Infrastructure backup is enabled at Azure Stack Hub deployment time. A file share UNC path and credentials are required
  After deployment, backup can also be enabled using UI or APIs
  Note: Traditional backup using Microsoft Data Protection Manager and Hyper-V capabilities are not used by Infrastructure Backup Controller

## Slide 24: Considerations
Allocate at least 1Tb per Azure Stack Hub cloud
  Recommendation: Keep at most 7 days of backups on the share. Manually archive or discard anything older than 7 days.
Neither Azure Files nor Azure Blob storage are supported
Encryption key must be stored external to the stamp
  Recommendation: Use KeyVault in Azure to store the secret
Infrastructure Backup Service best practices - Azure Stack Hub | Microsoft Docs

## Slide 25: Infrastructure backup - released and planned updates
Configurable retention period and backup frequency
Automatic deletion of stale backups
New and improved alerts
Enable/disable automatic backups
Automatic
Backups
Certificate wrapped key encryption
Validate infrastructure backups using ASDK
No interruption to production deployment
Support for AAD and ADFS
Use public key in certificate to encrypt unique symmetric key generated with each backup
Provide private portion during recovery only.
Cloud recovery
on ASDK

## Slide 26: Backup of HLH and switches
Azure Stack Hub
Operator
User
Azure Stack Hub Infrastructure
IaaS
PaaS
HLH
ToR and BMC
switches
External
File Share
Manually triggered via OEMs tools or scripts
OEMs will provide guidance to determine when restore from backup is necessary vs. configuration

## Slide 27: Azure Stack Hub cloud recovery
Goal: Recover your Azure Stack Hub infrastructure and user configuration after catastrophic data loss
OPERATOR
MANAGED SERVICE/USER
HARDWARE PARTNER
Phase1
Phase2
PaaS restore
Phase3
IaaS VM restored
Phase4
User data restored
Phase 0
HW ready
Cloud recovery
Phases: Recovery is separated into atomic phases that build on each other
  Phase 0: Get the hardware ready
  Phase 1: Cloud recovery - Restore Azure Stack Hub’s “personality”
  Phase 2: Restore PaaS resources and data
  Phase 3: Restore user IaaS VMs
  Phase 4: Recover user data
Order  manufacturing  delivery  Prof services on-site
Weeks
<1 week
Days
Hours to days to weeks
Prof services on-site

## Slide 28: Restore process
With catastrophic data loss but the hardware is still usable, redeployment of Azure Stack Hub is required. During redeployment, you can specify the storage location and credentials required to access backups.
Deployment mode | Starting point | End point
Clean install | Baseline build | OEM deploys Azure Stack Hub and updates to the latest supported version.
Recovery mode | Baseline build | OEM deploys Azure Stack Hub in recovery mode and handles the version matching requirements based on the latest backup available. The OEM completes the deployment by updating to latest supported version.
Recover from catastrophic data loss in Azure Stack Hub - Azure Stack Hub | Microsoft Docs

## Slide 29: Contents of an infrastructure backup
Internal identity services
Backup of internal domain controller
Used to seed the domain in the new deployment
Deployment configuration
Deployment ID
Deployment parameters
CA root certificate
ADFS configuration
User subscriptions
- Admin/default subscriptions re-created during deployment
Original Plans/offers
Previously defined quotas for
  Storage
  Network
  Compute
Key vault secrets
User RBAC roles and policies
RBAC for default subscription not restored
Resource groups
Not included in backup
Any resource group present after restore was recreated during the hydration of resources. Any meta-data about the resource group is not restored (e.g. tags)
What is included and not in an Azure Stack Infrastructure backup

## Slide 30: Testing infrastructure restore with the ASDK
Want to test your infrastructure backup?
  Prepare an Azure Stack Hub Development Kit (ASDK) host server using the current version of Azure Stack Hub
  Copy the backup to a local folder on the ASDK
  Deploy the ASDK in cloud recovery mode using the InstallAzureStackPOC.ps1 script
  After a successful cloud recovery deployment, you need to complete the restore using the Restore-AzureStack cmdlet
Use the ASDK to validate an Azure Stack backup - Azure Stack Development Kit (ASDK) | Microsoft Docs

## Slide 31: HA and DR patterns

## Slide 32: Disaster recovery between Azure Stack Hub and Azure
Azure
Stack
Azure
Service Provider
On-premises
Azure Site
Recovery
Azure Backup
SQL IaaS
Azure App Service
SQL IaaS
Azure App Service
Azure/SP services
Partner Backup
Partner Site Recovery
Azure/SP services
Partner Backup
Partner Site Recovery

## Slide 33: Application availability between Azure Stack Hub and Azure Stack Hub (short distance/shared impact radius)
Azure
Stack
Azure
Stack
Site A
High Availability: Yes
Disaster recovery: No

## Slide 34: Disaster recovery between Azure Stack Hub and Azure Stack Hub (long distance/separate failure domains)
Azure
Stack
Azure
Stack
Site A
Disaster recovery
Site B
Failure Domain
Failure Domain
What is your data loss tolerance?
What is your downtime tolerance?
Longer Distance
Higher Latency
Lower Bandwidth
Higher Data loss

## Slide 35: Azure Stack Hub Deployment Patterns
Azure Stack Hub
Managed Services Provider
Cloud user
I can protect applications deployed on IaaS
I can create a protection strategy for PaaS based
I can recover Azure Stack Hub infrastructure

## Slide 36: SQL: Multiple Deployments
Asynchronous
Site A
Site B
Load Balancer
Disaster recovery
HA
Web App
SQL HA
SQL Always On

## Slide 37: SQL site to site recovery behind VPN
Site 2 Site VPN
Availability Set
Subnet
Availability group
Synchronous
Asynchronous
Active
Directory
Domain
name server
Site A
Site B
Virtual Network
Virtual Network
Load Balancer
Site 2 Site VPN
Availability group listeners
Accounts synchronized
Disaster recovery
HA
Web App
Learnings

## Slide 38: SQL distributed availability group
Availability group
Synchronous
Asynchronous
Site A
Site B
Load Balancer
Availability group listeners
Forwarder is empty
Load Balancer
Disaster recovery
HA
Availability group
Synchronous
Distributed group
HA
Primary
Forwarder
Learnings
Web App

## Slide 39: App Service: Multiple deployments
Learnings
Site A
Site B
Load Balancer
Separate instance of RP
For DR: Redeploy app and restore user database
Use distributed group for application to be HA
Disaster recovery
HA
File content
File content
App Service Component
User App
SQL HA
SQL HA
SQL HA
SQL HA
File content
File content
App Service Component
User App
SQL HA
SQL HA
SQL HA
SQL HA
Distributed group on the application layer e
HA

## Slide 40: Recovery Time Planning
Azure Stack Hub integrated system
Azure Stack Hub integrated system
Backup
Automatic Failover
Hours to Days
Replication/ snapshot
Active
Minutes to hours
Seconds to minutes
Active
Warm
Zero
High availability
Fault tolerance
Manual Failover/ Re-deployment
Restore
Public Azure
Always available
Fully deployed and registered
Or
Wait for hardware partner to deliver new integrated system

## Slide 41: User VM Protection

## Slide 42: Data protection and recovery options
Azure Stack Hub
Operator
User
On-prem/remote
target
Azure Stack Hub Infrastructure
IaaS
PaaS
HLH
ToR and BMC
switches
Can perform backup using standard on-premises tools, or cloud based offerings like Azure backup
Azure Site Recovery supports failover and failback

## Slide 43: User IaaS VM backup/restore
Secure connections using S2S VPN and ExpressRoute
Azure Stack Hub
Service Provider
Public Azure
Azure Stack Hub Customer
Service Provider
Use existing products on-prem or remote
Tenant driven workflows
Application, file/folder, and page-blob snapshot level snapshot
Support for Microsoft and 3rd party products
Existing backup tools can target several backup targets…

## Slide 44: Support for IaaS VM backup/restore
Azure Backup supports backup and restore of IaaS VM
    Support for live backup with no OS downtime (requires IaaS VM Extension)
    Supports incremental and full backups of IaaS VMs
    Supports ability to restore the IaaS VM instance (model) and virtual disks
Azure Stack Hub does not currently support the necessary storage APIs to enable IaaS VM backup
    This is a well-known gap which forces the use of guest level backup
    The decision is to focus on enabling Azure consistent backup and restore of IaaS VMs instead of implementing a stop gap/temporary that may break consistency
Partners can use the same APIs to enable backup/restore scenarios
    Fosters a consistent model across Azure and Azure Stack Hub for ISVs integrating with Azure Stack Hub
Protect VMs deployed on Azure Stack Hub - Azure Stack Hub | Microsoft Docs

## Slide 45: Microsoft Azure Backup server
Azure Backup requires a backup server VM
    Install an Azure Backup Server VM in Azure Stack Hub
    Add storage for local backups to the Azure Stack Hub VM
    Select VMs to be protected
    Choose short-term (local protection) and/or long-term protection (to Azure storage)
Install Azure Backup Server on Azure Stack - Azure Backup | Microsoft Docs

## Slide 46: Support for IaaS VM replication - Summary
Azure Site Recovery supports replication of IaaS VM
    Support for live backup with no OS downtime
    Supports low RTO to Azure
    Supports planned, unplanned, and test failover of IaaS VM instance (model and data)
Azure Stack Hub GA does not support the necessary storage APIs to enable IaaS VM replication
    This is a well-known gap which forces the use of guest level replication
    The decision is to focus on enabling Azure consistent replication and failover of IaaS VMs instead of implementing a stop gap/temporary that may break consistency
Partners can use the same APIs to enable replication and failover scenarios
    Fosters a consistent model across Azure and Azure Stack Hub for ISVs integrating with Azure Stack Hub

## Slide 47: Azure Stack Hub BC/DR partners
Partner - product name | Validation complete | More information
Azure Backup Server | Complete | https://azure.microsoft.com/en-us/blog/backup-your-applications-on-azure-stack-with-azure-backup/
Azure Site Recovery | Complete | https://docs.microsoft.com/en-us/azure/site-recovery/azure-stack-site-recovery
Acronis | Complete | https://acronis.com/business/backup
Actifio | Complete | https://www.actifio.com/azure-stack-data-protection
Carbonite | Complete | https://www.carbonite.com/data-protection/high-availability/
Commvault | Complete | https://www.commvault.com/solutions/by-technology/virtual-machine-and-cloud/microsoft-azure
Dell EMC | Complete | https://www.dellemc.com/en-us/solutions/cloud/microsoft-azure-stack.htm
Micro Focus | Complete | Press Release
Quest | Complete | Blog post
Rubrik | Complete | https://www.rubrik.com/solutions/azure-stack/
Veritas | Complete | https://www.veritas.com/solution/microsoft-cloud
ZeroDown | Complete | http://www.zerodownsoftware.com/azure-stack/
https://azure.microsoft.com/en-us/blog/protecting-applications-and-data-on-azure-stack/

## Slide 48: Protecting IaaS VMs in Availability Sets

## Slide 49: Availability sets for IaaS VMs
In this case, we want to have protection for a multi-server VM environment using a load balancer and an availability set
Azure Stack Hub
Operator
User
Azure Stack Hub Infrastructure
IaaS
PaaS
HLH
ToR and BMC
switches

## Slide 50: Availability sets and backup/restore
Scenarios
  1 - Increase application availability in the event of planned maintenance
  2 - Increase application availability in the event of unplanned failures/maintenance
Application patterns
  Availability sets are ideal for stateless apps that can scale-in/out Applications that work well behind a load balancer
  Application data is typically external to the IaaS VM
IaaS
PaaS
Infra
Archive
Backup implications
  Protecting individual VMs does not guarantee complete application data set is captured with consistency.
  Need to focus on protecting the application data repository(ies)
  Deployment code takes care of OS boot/config

## Slide 51: Protecting PaaS in Azure Stack Hub

## Slide 52: Protecting PaaS data stores
Azure Stack Hub
Operator
User
Azure Stack Hub Infrastructure
IaaS
PaaS
HLH
ToR and BMC
switches
PaaS BC/DR is application dependent. The focus is on building a process to take a consistent backup and perform a consistent restore.

## Slide 53: PaaS storage archiving (without cool storage)
Automated migration
  Azure Backup, 3rd party backup/migration products, StorSimple
Manual migration
  AzCopy, .Net Library, REST API, Client Library
Cool Storage in Azure Stack Hub
  No plans
IaaS
PaaS
Infra
Archive

## Slide 54: DevOps and BC/DR in Azure Stack Hub

## Slide 55: DevOps and BC/DR
http://www.cio.com/article/3075277/disaster-recovery/how-to-master-disaster-recovery-in-a-devops-world.html
https://devops.com/companys-disaster-waiting-happen/
https://www.actifio.com/company/blog/post/6-questions-you-need-to-be-asking-about-your-disaster-recovery-plan/
http://www.computerworld.com.au/article/593813/devops-vs-itil/
http://searchservervirtualization.techtarget.com/feature/How-should-organizations-approach-the-DevOps-movement
Fast fail and rapid recovery
Parameterized deployment scripts and location agnostic templates
Optimizing compute/storage utilization and cost reduction
Implement and test resiliency and fault detection
Continuously test backup and DR strategies
Validate data integrity, consistency, and availability
Match DevOps principles with mature ITIL processes
Modernize outdated, expensive, and fragile BC/DR strategies

## Slide 56: General guidance
Design resilient applications
Azure Paired Regions
Availability Checklist
Retry general guidance
Retry service specific guidance

## Slide 57: Links to other resources
Ignite 2018
BRK3335 session
SQL Server on Azure VMs
Overview
Configure high availability
    HA and DR options
    Configuring Always On availability group
Protecting data
    Backup and restore
    Automated backup
    Using Azure storage for backup
Application patterns
App Services
  Overview
  Backup your app in Azure
  Geo Distributed Scale
  Automate backup and restore

## Slide 58: Questions?